## Slide 1: Video Measurement of Golf Green Putting Speed Using a Cellphone
Joe Sommer, Tim Lulis, John Kaminski
Mechanical Engineering and Plant Science
The Pennsylvania State University
experimental
kinematics
lab

## Slide 2
experimental
kinematics
lab
Weekend Project ?
27 Stimpmeter readings per day
Cellphone video
White ball on green background
Deceleration
s = v2 / 2 a

## Slide 3
experimental
kinematics
lab
Stimpmeter
Edward Stimpson 1935
USGA patent 2015 ($120)
Release ball at 20 degree angle
Measure ball roll distance (BRD) in feet
Consistent vLAUNCH
  1X notch, 6 ft/sec
  2X notch, 4.243 ft/sec

## Slide 4
experimental
kinematics
lab
Stimpmeter Reading - 6 rolls
Mark start location, roll 3 balls
  Not more than 8 inches apart
Mark first average location
Roll 3 balls in opposite direction
Mark second average location
Measure from start to first average
Measure from first to second average
Use mean of two distances
  Within 18 inches

## Slide 5
experimental
kinematics
lab
Methods
A4 bentgrass, flat
Trial 0
  1X notch, 100 BRD
Trial 1
  2X notch, 36 tests, 216 BRD
  Develop computational model
Trial 2
  2X notch, 37 tests, 222 BRD
  Validate model

## Slide 6
experimental
kinematics
lab
Trial 0
1X notch, 100 rolls, same location, no video
RMSE 3.93 inch
0.2 inch/roll
plastic
deformation
Rana, Askew
(2017)

## Slide 7
experimental
kinematics
lab
Video Photogrammetry
iPhone 6 back camera
  30 fps video, 1920x1080 pixels
42 inches above turf, level
  40 inch FOV
  48 pix/inch
Random locations
  Start/middle/end
  Stimpmeter not visible
  OK to stop in FOV

## Slide 8
experimental
kinematics
lab
Video Analysis
Personal computer using MATLAB
Binarize
  Mean intensity + two stdev
  Morphological open/close 10x10
Blob analysis
  Centroid location in pixels
  Area in pixels (affected by shadow)
Boundary analysis
  Circle fit
  Ball diameter in pixels

## Slide 9
experimental
kinematics
lab
Video Results

## Slide 10
experimental
kinematics
lab
Kinematics
Pixels per inch
  Camera calibration for initial analysis
  Mean ball diameter in pixels / 1.68 inch
X-Y location in inches versus time
  Blob centroid, not center for circle fit
Savitsky-Golay 7-point floating cubic interpolant
  Position, velocity and acceleration

## Slide 11
experimental
kinematics
lab
Linear Velocity - Model
Pure rolling, constant deceleration
v = p1 t + p2 a = -p1
sLIN_VEL = (vLAUNCH)2 / 2 a
Typical values for 1X notch
  vLAUNCH = 6 ft/sec, a = 1.5 ft/sec2, sLIN_VEL = 12 ft
accel is function of vel
  Hubbard, Alaways (1999)
  Brearly, deMestre (2004)

## Slide 12
experimental
kinematics
lab
Linear Velocity - Results
fit velocity as linear function of time
slope is decel
higher decel higher vel
lower slope
lower vel

## Slide 13
experimental
kinematics
lab
Linear Velocity - Predictions
fit velocity as linear function of time
Trial 1
2X notch
30 fps
N = 216

## Slide 14
experimental
kinematics
lab
Alternate Models
Quadratic velocity
  v = p1 t2 + p2 t + p3
Cubic position
  x = p1 t3 + p2 t2 + p3 t + p4
Linear drag ODE
  a = p1 v + p2
Quadratic drag ODE
  a = p1 v2 + p2

## Slide 15
experimental
kinematics
lab
Quadratic Velocity - Predictions
fit velocity as quadratic function of time
Trial 1
2X notch
30 fps
N = 216

## Slide 16
experimental
kinematics
lab
Cubic Position - Predictions
fit position as cubic function of time
Trial 1
2X notch
30 fps
N = 216

## Slide 17
experimental
kinematics
lab
Linear Drag ODE - Predictions
fit acceleration as linear function of velocity
Trial 1
2X notch
30 fps
N = 216

## Slide 18
experimental
kinematics
lab
Quadratic Drag ODE - Predictions
fit acceleration as quadratic function of velocity
Trial 1
2X notch
30 fps
N = 216

## Slide 19
experimental
kinematics
lab
Correlation Model
Residuals correlated to vMEAN during video
BRD = C1 + C2 sLIN_VEL + C3 vMEAN + C4 (p1)QUAD_VEL

## Slide 20
experimental
kinematics
lab
Correlation Model - Predictions
sLIN_VEL
(p1)QUAD_VEL
Trial 1
2X notch
30 fps
N = 216
RMSE 3.87 inch
BRD = C1 + C2 sLIN_VEL + C3 vMEAN + C4 (p1)QUAD_VEL

## Slide 21
experimental
kinematics
lab
Correlation Model - Validation
Trial 1
2X notch
30 fps
N = 216
Trial 2
2X notch
30 fps
N = 222
total
RMSE 4.45 inch

## Slide 22
experimental
kinematics
lab
Stimpmeter - Validation
Trial 1
N = 36
Trial 2
N = 37
overall
RMSE 3.73 inch

## Slide 23
experimental
kinematics
lab
Conclusions
iPhone, iPad and Android
  Tripod mount, level
  Putt into FOV
Standard camera at 30 fps
  No special lighting
Ball diameter for photogrammetry
  Independent of camera height
95% confidence interval 7.5 inches
  Stimpmeter 3 rolls within 8 inches

## Slide 24
experimental
kinematics
lab
Future
Compass heading and GPS location
Measure break and consistency

## Slide 25
experimental
kinematics
lab
Consistent Break

## Slide 26
experimental
kinematics
lab
Stop in FOV - Velocity

## Slide 27
experimental
kinematics
lab
Stop in FOV - Row

## Slide 28
experimental
kinematics
lab
Stop in FOV - Break

## Slide 29
experimental
kinematics
lab
Quadratic Velocity

## Slide 30
experimental
kinematics
lab
Cubic Position

## Slide 31
experimental
kinematics
lab
Linear Drag ODE

## Slide 32
experimental
kinematics
lab
Quadratic Drag ODE